## Slide 1: Verilog Lab 1
Prof. Shih-Chieh Chang
Logic Design 2022 spring

## Slide 2: Outline
Workstation setting: MobaXterm
Project

## Slide 3: Outline
Workstation setting: MobaXterm
Project

## Slide 4: MobaXterm Download
Download the free version of MobaXterm
  https://mobaxterm.mobatek.net/download-home-edition.html

## Slide 5: Workstation Setup

## Slide 6: Workstation Setup (Cont.)
Enter the following blank
  Remote host: nthucad.cs.nthu.edu.tw
  Specify username: (your account)
  Port: 22
Click “OK”

## Slide 7: Login at the First Time
Key in your initial password from e mail

## Slide 8: Change your Password
Type “passwd” to change your password

## Slide 9: Connecting to Workstation
Find a workstation with less users

## Slide 10: Connecting to Workstation (Cont.)
Connect to a work station
  ssh -X icXX (XX should be 21~58)

## Slide 11: Connecting to Workstation (Cont.)

## Slide 12: Create directory
Right click to create new directory “example”
or by command line “mkdir example”

## Slide 13: Create directory
1.
2.

## Slide 14: Uploading Files
Upload files
  Upload your files by dragging them in to directory

## Slide 15: Edit files in workstation
Right click open with mobaXterm’s editor
Vim is available in workstation
You can also edit in Windows then upload it

## Slide 16: Run simulation
Use NC verilog as standard simulation platform
You can use any IDE/Editor to program

## Slide 17: Run simulation (Cont.)
$ ncverilog all.v file you need
  i.e. $ ncverilog Test_Bench.v Simulator.v

## Slide 18: Run simulation (Cont.)

## Slide 19: Outline
Workstation setting: MobaXterm
Project

## Slide 20: 4 bit Ripple Carry Adder

## Slide 21: Rules
, are unsigned numbers
Only basic logic gates are ALLOWED (and, or, nand, nor, not ) ,no xor & xnor
Please AVOID using
1. Continuous assignment and conditional operators
2. Behavioral operators (e.g., +, -, &, |, ^, &&, !, ~….., etc.)
3. Behavioral operators are ALLOWED in your TESTBENCH
Edit your own testbench

## Slide 22: Please Follow The Format Below
module Ripple_Carry_Adder (in0, in1, out,cout,s_overflow,u_overflow);
input [4-1:0] in0;
input [4-1:0] in1;
output [4-1:0] out;
output cout;
output s_overflow;
output u_overflow;
// here is your design
endmodule

## Slide 23: Submission
Lab 1 code submission due date & time: 2022/04/07,11:59pm
Please submit your Verilog codes to eeclass
  Lab1_YourStudentID_Codes.v
We will test your codes by our own testbench